Speedup – T1 = T = S = Sequential time to execute a program
TP = Time to execute the same program with p processors
Speedup = SP = T1 / TP
Efficiency – Ep = Speedup / P
Realistic Speedup – σ = sequential fraction of the program
π = parallel portion of the program
o = parallel overhead
TP = σ + (o + π ) / P
SP = 1 / ( σ + (o + π) / P )
SIMD = One control unit, many processing elements, PE interconnection.
MIMD = Multiple processors, each executing its own code.
4 Major Prarallel Programming Steps - Partition, Communicate, Agglomerate, mapping
Implicit – The compiler detects parallelism
Explicit – Programmer expresses parallelism
Roofline – Sets an upper bound on performance of a kernel depending on the kernel’s operation intensity. If we think of operation intensity as a column that hits the roof, either it hits the flat part of the roof, meaning performance is compute-bound or performance is ultimately memory-bound.
Cache Misses:
Compulsory – Cold start miss, first reference miss, first access
Capacity – Blocks are discarded from cache because cache cant contain all blocks
Conflict – Conflict misses occur when several blocks are mapped to the same set, also called collision misses or interference misses
3 important functions – exp, poly, log
Knapsack:
Input: N, CAP, w[], p[]
for (item = 1; item < N; item++){
for (weight = 0; weight < CAP; weight++){
itemWeight = w[item];
itemProfit = p[item] + M[item-1][weight-itemWeight];
previousProfit = M[item-1][weight];
 if (itemWeight > weight) {
M[item][weight] = previousProfit;
}
else if (previousProfit > itemProfit)
M[item][weight] = previousProfit;
}
else {
M[item][weight] = itemProfit;
}
}
}

return M[N][CAP];